Modes of operation of timers
Normal mode : start the timer , as the timer reaches the maximum value it overflows ,generate the interrupt if enabled ,set the	corresponding timer overflow flag .
The timer will continue to run unless u stop it	or u reach the end of the program

---
 compare mode & waveform generation
There is a 8 bit comparator that continuously compares the value in the TCNT2 and OCR2	when ever TCNT2 equals OCR2 the comparator signals a match .
it will set the corresponding flag
will generate the interrupt if enabled

---
Register

---
Registers

---
what are the two possibility that can happen ?
When there is a match we can clear the contents of the TCNT2 . this is nothing but clear the timer on compare match mode .
Let the timer run and overflow.

---
Com bits

---
Timers can also be used for PWM generation
Fast PWM mode
Phase correct PWM mode

---
Phase correct PWM mode
It is based on the dual slope operation
The timer in this case act as count up & count down timer .
The resolution is fixed to the 8 bits
the timer overflow flag will be set when the timer reaches the bottom value .
The pwm is generated on OC2pin.

---
Fast PWM
It provides a high frequency PWM wave form generation .
It has a single slope operation .
The counter counts from bottom to max then then restart from bottom.

---
Refer datasheet .>>>
Page no. 104 – 120 for timer2(8 bit timer)