Data communication
Some Embedded systems cannot work in isolation.
They may need to communicate with the other systems.
Two approaches of the communication is possible.
Serial communication & parallel communication.

---
Continued...
A bit is transmitted at a single time
Slower	[ ↓ ]
Few wires	[ ↑ ]
Byte or more at a time.	[ ↑ ]
Faster	[ ↑ ]
Large wire	[ ↓ ]
Sender
Reciever
Sender
Receiver

---
Serial data transmission type
Transmission only in one direction
Data transmitted in one direction
Direction of data can be changed
Both direction & simultaneously
Simplex
DUPLEX
FULL DUPLEX

---
Serial com transmission mode
Synchronous mode
Asynchronous mode

---
Asynchronous mode
Transmit one character at a time
Data bits in a character ?
Order of transmission LSB to MSB
Start and stop bits tells receiver where one character stops and other starts
Stop bits can be either one or two
Parity bit for error detection
Sending parity bit is optional

---
frame format

---
Async.. serial transfer
NO data- signal is kept high
Start bit – signal low for 1 bit time
The data transmission rates are specified in terms of Baud rate
Common values	2400,9600,19200,57600,115200
Baud rate

---
Atmega8 USART facts
Full duplex operation	(independent receive and transmit register)
High resolution baud rate register	(UBRR)
Serial frames with 5 -9 data bits	( 1-2 stop bits ,odd even parity generator,checking by H/W)
Errors	data overrun :data loss due to receive buff full	frame error : error in the stops bits received	Parity error:

---
Parity Bit
A parity bit is a bit that is added to ensure that the number of bits with value of one in a given set of bits is always even or odd.
Parity bits are used as the simplest error detecting code.

---
Registers

---
Registers

---
Baud Rate register

---
Equations

---
Uart Init

---
Transmit function

---
Refer>>>
page no (for usart registers) 153 – 159
page no 133 -159